## Slide 1: Operating System Principles: Devices, Device Drivers, and I/O CS 111 Operating Systems Peter Reiher

## Slide 2: Outline
Devices and device drivers
I/O performance issues
Device driver abstractions

## Slide 3: So You’ve Got Your Computer . . .
It’s got memory, a bus, a CPU or two
But there’s usually a lot more to it than that
And who knows what else?

## Slide 4: Welcome to the Wonderful World of Peripheral Devices!
Our computers typically have lots of devices attached to them
Each device needs to have some code associated with it
  To perform whatever operations it does
  To integrate it with the rest of the system
In modern commodity OSes, the code that handles these devices dwarfs the rest

## Slide 5: Peripheral Device Code and the OS
Why are peripheral devices the OS’ problem, anyway?
Why can’t they be handled in user-level code?
Maybe they sometimes can, but . . .
Some of them are critical for system correctness
  E.g., the disk drive holding swap space
Some of them must be shared among multiple processes
  E.g. screen; Which gets often rather complex
Some of them are security-sensitive
Perhaps more appropriate to put the code in the OS

## Slide 6: Where the Device Driver Fits in
At one end you have an application
  Like a web browser
At the other end you have a very specific piece of hardware
  Like an Intel Gigabit CT PCI-E Network Adapter
In between is the OS
When the application sends a packet, the OS needs to invoke the proper device driver
Which feeds detailed instructions to the hardware

## Slide 7: Device Drivers
Generally, the code for these devices is pretty specific to them
It’s basically code that drives the device
  Makes the device perform the operations it’s designed for
So typically each system device is represented by its own piece of code
The device driver
A Linux 2.6 kernel came with over 3200 of them . . .

## Slide 8: Typical Properties of Device Drivers
Highly specific to the particular device
  System only needs drivers for devices it hosts
Inherently modular
Usually interacts with the rest of the system in limited, well defined ways
Their correctness is critical
  Device behavior correctness and overall correctness
Generally written by programmers who understand the device well
  But are not necessarily experts on systems issues

## Slide 9: Abstractions and Device Drivers
OS defines idealized device classes
  Disk, display, printer, tape, network, serial ports
Classes define expected interfaces/behavior
  All drivers in class support standard methods
Device drivers implement standard behavior
  Make diverse devices fit into a common mold
  Protect applications from device eccentricities
Abstractions regularize and simplify the chaos of the world of devices

## Slide 10: What Can Driver Abstractions Help With?
Encapsulate knowledge of how to use the device
  Map standard operations into operations on device
  Map device states into standard object behavior
  Hide irrelevant behavior from users
  Correctly coordinate device and application behavior
Encapsulate knowledge of optimization
  Efficiently perform standard operations on a device
Encapsulate fault handling
  Understanding how to handle recoverable faults
  Prevent device faults from becoming OS faults

## Slide 11: How Do Device Drivers Fit Into a Modern OS?
There may be a lot of them
They are each pretty independent
You may need to add new ones later
So a pluggable model is typical
OS provides capabilities to plug in particular drivers in well defined ways
Then plug in the ones a given machine needs
Making it easy to change or augment later

## Slide 12: Layering Device Drivers
The interactions with the bus, down at the bottom, are pretty standard
  How you address devices on the bus, coordination of signaling and data transfers, etc.
  Not too dependent on the device itself
The interactions with the applications, up at the top, are also pretty standard
  Typically using some file-oriented approach
In between are some very device specific things

## Slide 13: A Pictorial View
App 1
App 2
App 3
User space
Kernel
space
Hardware
USB bus controller
PCI bus controller
USB
bus
PCI
bus
Device
Drivers
System
Call
Device
Call

## Slide 14: Device Drivers Vs. Core OS Code
Device driver code is in the OS, but . . .
What belongs in core OS vs. a device driver?
Common functionality belongs in the OS
  Caching
  File systems code not tied to a specific device
  Network protocols above physical/link layers
Specialized functionality belongs in the drivers
  Things that differ in different pieces of hardware
  Things that only pertain to the particular piece of hardware

## Slide 15: Devices and Interrupts
Devices are primarily interrupt-driven
  Drivers aren’t schedulable processes
They work at different speed than the CPU
  Typically slower
They can do their own work while CPU does something else
They use interrupts to get the CPU’s attention

## Slide 16: Devices and Busses
Devices are not connected directly to the CPU
Both CPU and devices are connected to a bus
Sometimes the same bus, sometimes a different bus
Devices communicate with CPU across the bus
Bus used both to send/receive interrupts and to transfer data and commands
  Devices signal controller when they are done/ready
  When device finishes, controller puts interrupt on bus
  Bus then transfers interrupt to the CPU
  Perhaps leading to movement of data

## Slide 17: CPUs and Interrupts
Interrupts look very much like traps
  Traps come from CPU
  Interrupts are caused externally to CPU
Unlike traps, interrupts can be enabled/disabled by special CPU instructions
  Device can be told when they may generate interrupts
  Interrupt may be held pending until software is ready for it

## Slide 18: The Changing I/O Landscape
To quote a recent Nobel Prize winner, “the times they are a’changing”
Storage paradigms
  Old: swapping, paging, file systems, data bases
  New: NAS, distributed object/key-value stores
I/O traffic
  Old: most I/O was disk I/O
  New: network and video dominate many systems
Performance goals:
  Old: maximize throughput, IOPS
  New: low latency, scalability, reliability, availability

## Slide 19: Device Performance
The importance of good device utilization
How to achieve good utilization

## Slide 20: Good Device Utilization
Key system devices limit system performance
  File system I/O, swapping, network communication
If device sits idle, its throughput drops
  This may result in lower system throughput
  Longer service queues, slower response times
Delays can disrupt real-time data flows
  Resulting in unacceptable performance
  Possible loss of irreplaceable data
It is very important to keep key devices busy
  Start request n+1 immediately when n finishes

## Slide 21: Poor I/O Device Utilization
IDLE
BUSY
I/O device
process
process waits to run
process does computation in preparation for I/O operation
process issues read system call, blocks awaiting completion
device performs requested operation
completion interrupt awakens blocked process
process runs again, finishes read system call
process does more computation
Process issues read system call, blocks awaiting completion

## Slide 22: How To Do Better
The usual way:
  Exploit parallelism
Devices operate independently of the CPU
So a device and the CPU can operate in parallel
But often devices need to access RAM
  As does the CPU
How to handle that?

## Slide 23: What’s Really Happening on the CPU?
Modern CPUs try to avoid going to RAM
  Working with registers
  Caching on the CPU chip itself
If things go well, the CPU doesn’t use the memory bus that much
  If not, life will be slow, anyway
So one way to parallelize activities is to let a device use the bus instead of the CPU

## Slide 24: Direct Memory Access (DMA)
Allows any two devices attached to the memory bus to move data directly
  Without passing it through the CPU first
Bus can only be used for one thing at a time
So if it’s doing DMA, it’s not servicing CPU requests
But often the CPU doesn’t need it, anyway
With DMA, data moves from device to memory at bus/device/memory speed

## Slide 25: Keeping Key Devices Busy
Allow multiple requests to be pending at a time
  Queue them, just like processes in the ready queue
  Requesters block to await eventual completions
Use DMA to perform the actual data transfers
  Data transferred, with no delay, at device speed
  Minimal overhead imposed on CPU
When the currently active request completes
  Device controller generates a completion interrupt
  OS accepts interrupt and calls appropriate handler
  Interrupt handler posts completion to requester
  Interrupt handler selects and initiates next transfer

## Slide 26: Interrupt Driven Chain Scheduled I/O
xx_read/write() {
allocate a new request descriptor
fill in type, address, count, location
insert request into service queue
if (device is idle) {
disable_device_interrupt();
xx_start();
enable_device_interrupt();
}
await completion of request
extract completion info for caller
}
xx_start() {
get next request from queue
get address, count, disk address
load request parameters into controller
start the DMA operation
mark device busy
}
xx_intr() {
extract completion info from controller
update completion info in current req
wakeup current request
if (more requests in queue)
xx_start()
else
mark device idle
}

## Slide 27: Multi-Tasking & Interrupt Driven I/O
device
1A
process 1
1A
P1 runs, requests a read, and blocks
P2 runs, requests a read, and blocks
P3 runs until interrupted
Awaken P1 and start next read operation
P1 runs, requests a read, and blocks
P3 runs until interrupted
process 2
process 3
2A
1B
2B
1B
1C
2A
2B
7. Awaken P2 and start next read operation
8. P2 runs, requests a read, and blocks
9. P3 runs until interrupted
10. Awaken P1 and start next read operation
11. P1 runs, requests a read, and blocks

## Slide 28: Bigger Transfers are Better

## Slide 29: (Bigger Transfers are Better)
Disks have high seek/rotation overheads
  Larger transfers amortize down the cost/byte
All transfers have per-operation overhead
  Instructions to set up operation
  Device time to start new operation
  Time and cycles to service completion interrupt
Larger transfers have lower overhead/byte
  This is not limited to software implementations

## Slide 30: I/O and Buffering
Most I/O requests cause data to come into the memory or to be copied to a device
That data requires a place in memory
  Commonly called a buffer
Data in buffers is ready to send to a device
An existing empty buffer is ready to receive data from a device
OS needs to make sure buffers are available when devices are ready to use them

## Slide 31: OS Buffering Issues
Fewer/larger transfers are more efficient
  They may not be convenient for applications
  Natural record sizes tend to be relatively small
Operating system can consolidate I/O requests
  Maintain a cache of recently used disk blocks
  Accumulate small writes, flush out as blocks fill
  Read whole blocks, deliver data as requested
Enables read-ahead
  OS reads/caches blocks not yet requested

## Slide 32: Deep Request Queues
Having many I/O operations queued is good
  Maintains high device utilization (little idle time)
  Reduces mean seek distance/rotational delay
  May be possible to combine adjacent requests
  Can sometimes avoid performing a write at all
Ways to achieve deep queues:
  Many processes making requests
  Individual processes making parallel requests
  Read-ahead for expected data requests
  Write-back cache flushing

## Slide 33: Double-Buffered Output
buffer
#1
buffer
#2
application
device

## Slide 34: Performing Double-Buffered Output
Have multiple buffers queued up, ready to write
  Each write completion interrupt starts the next write
Application and device I/O proceed in parallel
  Application queues successive writes
    Don’t bother waiting for previous operation to finish
  Device picks up next buffer as soon as it is ready
If we're CPU-bound (more CPU than output)
  Application speeds up because it doesn’t wait for I/O
If we're I/O-bound (more output than CPU)
  Device is kept busy, which improves throughput
  But eventually we may have to block the process

## Slide 35: Double-Buffered Input
buffer
#1
buffer
#2
application
device

## Slide 36: Performing Double Buffered Input
Have multiple reads queued up, ready to go
  Read completion interrupt starts read into next buffer
Filled buffers wait until application asks for them
  Application doesn't have to wait for data to be read
When can we do chain-scheduled reads?
  Each app will probably block until its read completes
    So we won’t get multiple reads from one application
  We can queue reads from multiple processes
  We can do predictive read-ahead

## Slide 37: Scatter/Gather I/O
Many device controllers support DMA transfers
  Entire transfer must be contiguous in physical memory
User buffers are in paged virtual memory
  User buffers may be spread all over physical memory
  Scatter: read from device to multiple pages
  Gather: writing from multiple pages to device
Three basic approaches apply
  Copy all user data into contiguous physical buffer
  Split logical request into chain-scheduled page requests
  I/O MMU may automatically handle scatter/gather

## Slide 38: “Gather” Writes From Paged Memory
process virtual address space
physical memory
DMA I/O stream
user I/O
buffer

## Slide 39: “Scatter” Reads Into Paged Memory
process virtual address space
physical memory
DMA I/O stream
user I/O
buffer

## Slide 40: Memory Mapped I/O
DMA may not be the best way to do I/O
  Designed for large contiguous transfers
  Some devices have many small sparse transfers
    E.g., consider a video game display adaptor
Instead, treat registers/memory in device as part of the regular memory space
  Accessed by reading/writing those locations
For example, a bit-mapped display adaptor
  1Mpixel display controller, on the CPU memory bus
  Each word of memory corresponds to one pixel
  Application uses ordinary stores to update display
Low overhead per update, no interrupts to service
Relatively easy to program

## Slide 41: Trade-off: Memory Mapping vs. DMA
DMA performs large transfers efficiently
  Better utilization of both the devices and the CPU
    Device doesn't have to wait for CPU to do transfers
  But there is considerable per transfer overhead
    Setting up the operation, processing completion interrupt
Memory-mapped I/O has no per-op overhead
  But every byte is transferred by a CPU instruction
    No waiting because device accepts data at memory speed
DMA better for occasional large transfers
Memory-mapped better frequent small transfers
Memory-mapped devices more difficult to share

## Slide 42: Generalizing Abstractions for Device Drivers
Every device type is unique
  To some extent, at least in hardware details
Implying each requires its own unique device driver
But there are many commonalities
Particularly among classes of devices
  All disk drives, all network cards, all graphics cards, etc.
Can we simplify the OS by leveraging these commonalities?
By defining simplifying abstractions?

## Slide 43: Providing the Abstractions
The OS defines idealized device classes
  Disk, display, printer, tape, network, serial ports
Classes define expected interfaces/behavior
  All drivers in class support standard methods
Device drivers implement standard behavior
  Make diverse devices fit into a common mold
  Protect applications from device eccentricities
Interfaces (as usual) are key to providing abstractions

## Slide 44: Device Driver Interface (DDI)
Standard (top-end) device driver entry-points
  “Top-end” – from the OS to the driver
  Basis for device-independent applications
  Enables system to exploit new devices
  A critical interface contract for 3rd party developers
Some entry points correspond directly to system calls
  E.g., open, close, read, write
Some are associated with OS frameworks
  Disk drivers are meant to be called by block I/O
  Network drivers are meant to be called by protocols

## Slide 45: DDIs and sub-DDIs
Basic I/O
read, write,
seek, ioctl,
select
Life Cycle
initialize, cleanup
open, release
Common DDI
Disk
request
revalidate
fsync
Network
receive,
transmit
set MAC
stats
Serial
receive character
start write
line parms

## Slide 46: Standard Driver Classes & Clients
file & directory
operations
networking & IPC
operations
direct device
access
system calls
UNIX FS
DOS FS
CD FS
block I/O
TCP/IP
X.25
PPP
data Link
provider
display class
serial class
tape class
disk class
CD
drivers
disk
drivers
tape
drivers
display
drivers
serial
drivers
NIC
drivers
device driver interfaces (*-ddi)

## Slide 47: Drivers – Simplifying Abstractions
Encapsulate knowledge of how to use a device
  Map standard operations into operations onto device
  Map device states into standard object behavior
  Hide irrelevant behavior from users
  Correctly coordinate device and application behavior
Encapsulate knowledge of optimization
  Efficiently perform standard operations on a device
Encapsulation of fault handling
  Knowledge of how to handle recoverable faults
  Prevent device faults from becoming OS faults

## Slide 48: Kernel Services for device drivers
sub-class DDI
device driver
common DDI
memory
allocation
synchronization
error reporting
run-time
loader
I/O resource
management
DMA
buffering
DKI – driver/kernel interface
configuration

## Slide 49: Driver/Kernel Interface
Specifies bottom-end services OS provides to drivers
  Things drivers can ask the kernel to do
  Analogous to an ABI for device driver writers
Must be very well-defined and stable
  To enable 3rd party driver writers to build drivers
  So old drivers continue to work on new OS versions
Each OS has its own DKI, but they are all similar
  Memory allocation, data transfer and buffering
  I/O resource (e.g. ports, interrupts) mgt, DMA
  Synchronization, error reporting
  Dynamic module support, configuration, plumbing

## Slide 50: Criticality of Stable Interfaces
Drivers are largely independent from the OS
  They are built by different organizations
  They might not be co-packaged with the OS
OS and drivers have interface dependencies
  OS depends on driver implementations of DDI
  Drivers depends on kernel DKI implementations
These interfaces must be carefully managed
  Well defined and well tested
  Upwards-compatible evolution

## Slide 51: Linux Device Driver Abstractions
An example of how an OS handles device drivers
Basically inherited from earlier Unix systems
A class-based system
Several super-classes
  Block devices
  Character devices
  Some regard network devices as a third major class
Other divisions within each super-class

## Slide 52: Why Classes of Drivers?
Classes provide a good organization for abstraction
They provide a common framework to reduce amount of code required for each new device
The framework ensure all devices in class provide certain minimal functionality
But a lot of driver functionality is very specific to the device
  Implying that class abstractions don’t cover everything

## Slide 53: Character Device Superclass
Devices that read/write one byte at a time
  “Character” means byte, not ASCII
May be either stream or record structured
May be sequential or random access
Support direct, synchronous reads and writes
Common examples:
  Keyboards
  Monitors
  Most other devices

## Slide 54: Block Device Superclass
Devices that deal with a block of data at a time
Usually a fixed size block
Most common example is a disk drive
Reads or writes a single sized block (e.g., 4K bytes) of data at a time
Random access devices, accessible one block at a time
Support queued, asynchronous reads and writes

## Slide 55: Why a Separate Superclass for Block Devices?
Block devices span all forms of block-addressable random access storage
  Hard disks, CDs, flash, and even some tapes
Such devices require some very elaborate services
  Buffer allocation, LRU management of a buffer cache, data copying services for those buffers, scheduled I/O, asynchronous completion, etc.
Important system functionality (file systems and swapping/paging) implemented on top of block I/O
Block I/O services are designed to provide very high performance for critical functions

## Slide 56: Network Device Superclass
Devices that send/receive data in packets
Originally treated as character devices
But sufficiently different from other character devices that some regard as distinct
Only used in the context of network protocols
  Unlike other devices
  Which leads to special characteristics
Typical examples are Ethernet cards, 802.11 cards, Bluetooth devices

## Slide 57: Identifying Device Drivers
The major device number specifies which device driver to use for it
Might have several distinct devices using the same drivers
  E.g., multiple disk drives of the same type
  Or one disk drive divided into logically distinct pieces
Minor device number distinguishes between those

## Slide 58: Accessing Linux Device Drivers
Done through the file system
Special files
  Files that are associated with a device instance
  UNIX/LINUX uses <block/character, major, minor>
    Major number corresponds to a particular device driver
    Minor number identifies an instance under that driver
Opening a special file opens the associated device
  Open/close/read/write/etc. calls map to calls to appropriate entry-points of the selected driver
brw-r----- 1 root operator 14, 0 Apr 11 18:03 disk0
brw-r----- 1 root operator 14, 1 Apr 11 18:03 disk0s1
brw-r----- 1 root operator 14, 2 Apr 11 18:03 disk0s2
br--r----- 1 reiher reiher 14, 3 Apr 15 16:19 disk2
br--r----- 1 reiher reiher 14, 4 Apr 15 16:19 disk2s1
br--r----- 1 reiher reiher 14, 5 Apr 15 16:19 disk2s2
A block special device
Major number is 14
Minor number is 0